## Slide 1: Recent researches on DNN accelerators and research plan
Kenshu Seto

## Slide 2: Brief introduction on Convolutional Neural Networks (CNNs)
Source:
Tutorial slides from “Hardware Architectures for Deep Neural Networks”, ISCA 2017
“Efficient Processing of Deep Neural Networks: A Tutorial and Survey,” V. Sze et al., Proceedings of the IEEE, 2017

## Slide 3: Convolutional Neural Networks (CNNs)
CNNs are very good at various image recognitions tasks.
  Each layer gets input images and generates output images
CNNs basically composed of only simple layers, that are,
  Convolution layer, Activation layer, Pooling layer, Padding layer…
Convolutions accounts for more than 90% of overall computation

## Slide 11: Convolution (CONVL) Layer computation (1 layer)
For each output pixel, do the following computation

## Slide 12: CONV Layer C Implementation (Nest depth of 7)
Opportunity for loop optimization
  loop tiling, interchange, were explored in many work, but not loop fusion
Can be used as a template for HLS

## Slide 13: Pooling (POOL) Layer
After pooling, image sizes shrink (mismatch in loop size)
  Not easy for loop fusion

## Slide 14: POOL Layer C Implementation (Nest depth of 6)
For CONV layer followed by POOL layer, it looks better to fuse these layers to reduce # execution cycles but loop rewriting is necessary to match loop structures for loop fusion.
R, S: pooling window size
U : stride

## Slide 15: Example CNN (VGG16, 2014)
Sequences of the same or similar CONV layers are used
  Can fuse them for faster execution with less RAMs

## Slide 16
Reducing

## Slide 17: Fused-Layer CNN Accelerators M. Alwani et al., (MICRO 2015)
Notes: This MICRO paper reduces the off-chip RAM access by placing the intermediate data between CNN layers on on-chip memory.

## Slide 18: Data transfers in VGG19
Large portions of data transfer are feature maps (fmaps) between layers
  Moving fmaps between off-chip and on-chip in accelerators results in high energy consumption
(note: VGG19 is a bit old. May exhibit different tendency in Recent DNN)

## Slide 19: Data transfers in VGG19
Reduce off-chip memory accesses to reduce energy
  Put fmaps in on-chip memory and use the data in on-chip memory
Feature maps (fmaps)
produced and consumed between layers should be on-chip RAMs and be reused to minimize the RAM size

## Slide 20: Main idea: Pyramid
output pixel 1 depends on tile(box)-shaped data from previous layers
  like a pyramid
All intermediate data are stored in on-chip RAMs instead of off-chip RAMs
Reuse on-chip data to reduce data-transfer
channel
Pyramid top
Pyramid base
Notes: In order to generate an output pixel 1, tile-shape of pixels in the preceding layers over channels are used. So, the required data to compute an output pixel become a pyramid-like shape. When next output pixel 2 is computed, we don’t need to load whole data of the tile 2, since we can reuse the data in tile 1. So, only the new data for the tile 2 can be loaded from memory.

## Slide 21: Proposed code for CONV layer
Simple C code
Move tile for
input/output
channels
loop of
tiled images
loop for kernel
Tiled input channel loop
Tiled output channel loop
Image tile size varies to reuse and save computation

## Slide 22: Area/Performance tradeoff of a CONV layer
Resource and cycles are estimated from C code
  Tile size Tm and Tn of output/input channels
Area constraint
Cycle counts
=
Tc
=
Tr

## Slide 23: Task-level pipelining and DSE
Each CONV layer becomes a pipeline stage
  Layers connected by ping-pong buffers
  Pipeline initiation interval(II) equals to max stage time
Minimizing “max stage time” by changing Tm and Tn
  Latency-minimized solution found by exhaustive search
Pipeline
II
Stage time
# pyramids
64*64
(for example)
Latency
Should shrink due to
computation reuse

## Slide 24: Implementation detail
Task-level pipelining by HLS pragma
Put “#pragma HLS dataflow”
Iterations for final output
pixels (Pyramid top points)
“reuse layers” copy data between
input/output buffers in successive layers

## Slide 25: Symbols used in the implementation code
Elaborately developed to maximize reuse
row, col:
Coordinate of
Pyramid top
Sx, Sy:
stride of the adjacent
pyramid base

## Slide 26: Inside the reuse layers
Output buffer of prev. layer are minimally copied to input buffer of next layer
Only new
data are
computed
Only new
data are
copied

## Slide 27: FPGA Evaluation with Vivado HLS
Compare two designs (Fused-layer, Baseline)for VGG19
  For fairness, match DSP resources between two designs
Fused-layer fused first 5 CONV layers in VGG19
  Including pooling layers, etc
Baseline iteratively execute each layer
  All feature maps stored in off-chip memory
  Use ping-pong buffers to overlap computation and I/O transfer
Matched
resources
rougly
the same
DRAM bandwidth
significantly
reduced

## Slide 28: Note on MICRO2015 paper
Pioneering work on fusing CNN layers for accelerator
  Successfully fused CNN layers with task-level pipelining
Buffer management is a bit complex but effective
Task level pipelining has similar effects as loop fusion

## Slide 29: Exploring Heterogeneous Algorithms for Accelerating Deep Convolutional Neural Networks on FPGAs. Xial et al., (DAC 2017)
Notes: This is an paper that proposes the use of line buffers between fused layers.
This paper also proposes method to generate optimal fused architecture (where to fuse, including where
To use Winograd) under resource constraints in FPGAs.

## Slide 30: Winograd algorithm for CONV layer
Reduces DSP (multiplier) units by ¼
  More complex and additions are necessary
But requires 4x higher bandwidth
Utilize Winograd algorithm in fused CNNs
“Evaluating Fast Algorithms for Convolutional Neural Networks on FPGAs,”, FCCM 2017

## Slide 31: Framework overview
Explained in the following slides
Vivado
HLS
#Block RAMs,
#DSP units
Off-chip bandwidth,
fusion architecture
Line buffer type
Previous type
Parametrized
library
Design Space
Exploration
Design
point
DNN spec.

## Slide 32: Proposed Design Space Exploration
Objective
  Minimize latency of total CNN execution
  Under constraints on Resource R and data-transfer T (in MB)
For each layer, determine
  Fusion group (layers in the same group are fused)
    execute in a pipelined manner
    reduce I/O bandwidth but increase RAM usage
    Different groups execute exclusively and share resources
  CONV algorithm type: Conventional or Winograd
  Parallelism
    Loop unroll factor, or # of data-path lanes
Solved by dynamic programming and branch-and-bound

## Slide 33: C code generation for HLS with templates
After design space exploration, optimal C code for HLS is generated with appropriate parameter setting

## Slide 34: Main idea: Use line buffer in Pyramid
Adopt Pyramid in MICRO2015 but without buffer management
  Computation reuse between pyramid not described (causes a lot of overhead)
Within Pyramid, line buffers are used
(ex. conv1)
channel x

## Slide 35: Result for VGG19 (First 5 conv + 2 pooling)
Used Vivado HLS
  C simulation, C-RTL cosimulation
  Compiled to ZC706 board
Transfer constraint
  2MB
    All layers must be fused
  32MB
    All feature maps can be stored in off-chip
With Winograd, higher performance achieved
Previous work [1]: MICRO2015 paper

## Slide 36: Result for AlexNet (5 CONV + 3 Pool)
    All layers fused
    Compared to MICRO2015, 1.24X speedup
      DSPs saved by Winograd algorithm are utilized by conventional CONV layers to enhance performance

## Slide 37: Note on DAC2017 paper
Extends MICRO2015 with line buffers in pyramids
  Buffer management in MICRO2015 not used
    No computational reuse between Pyramid
  RAM size seems to be reduced
  Detail of method and experiment unclear
Use Winograd algorithm in CONV layer
  Improve performance with area-efficient CONV layer
Possibly combine MICRO2015 pyramid with buffer management and line buffer?
  Enable computational reuse and buffer size reduction

## Slide 38: Research direction and plans

## Slide 39: Research objective

## Slide 40: General DNN accelerator environment
DNN
Description
HLS
RTL of
DNN
(Ideal)
DNN accelerator implementation
environment
Compiler backend
Code
for
GPU,
CPU,
distributed
computing
Parametrized
code/architectural
template
Programmable
DNN accelerator
Program for
DNN accelerator
Design Space
Explorer
Target &
resource &
constraints
description
RTL,
code
Target
scope
Looks
promising
Area?
DNN
Application
Development
Environment
(TensorFlow, Keras, …)
ASIC,
FPGA

## Slide 41: Overall picture
Action items
  Define DNN description (subset)
  Develop C templates
  Develop C code generator
  Optimize C code
  Develop analytical model for DSE
DNN
Description
C templates
conv, pool…
C code genarator
HLS
RTL of
DNN
C code
for DNN
Optimize
C code
Optimized
C code
Loop opt.
Memory opt.
(In future,
automation)
DSE
(Analytical model)
FPGA
ASIC
A subset of C code is used as
intermediate
language
Target &
resource &
constraints
description

## Slide 42: Related work

## Slide 43: Research plan
Develop template C code
  Easier for loop optimization (fusion) and memory optimization
  Conv (different strides with Activation), Pooling
Develop a generator tool
  that generate C code from DNN descriptions
  Keras can be used as DNN descriptions
Optimize the generated C code manually or semi-automatically
  Loop fusion, interchange, tiling, …
  Buffer optimization
Run Aladdin-gem5 for estimation
  only for single thread code
Synthesize with Vivado-HLS
  Use #pragma HLS DATAFLOW to do task level pipelining
  Implement the previous work (DAC2017, MICRO 2015) and compare the results (resource, #cycles, etc)

## Slide 44: CNN description in Keras
Simple and helpful to define a DNN description language

## Slide 45: Recent research on CNN accelerators

## Slide 46: Maestro / Maeri

## Slide 47: Tensor Comprehension

## Slide 48: Summary

## Slide 50: Research project at DRG: Design space exploration and memory access optimization for Deep Neural Network (DNN)

## Slide 51: Summary of the project
Problem
  Many accelerator exists, but mostly based on fixed templates
  DNN models are changing, so fixed template may be suboptimal
  Need to provide a efficient framework which generates the best DNN accelerator for ever-changing DNN models
Solution
  Given a DNN model, generate HLS and optimizer friendly C code
  With the code, explore design space and generate the best one
Key techniques
  Alladin-gem5
    System level performance estimation of accelerators with caches/scratchpads
    Explore DNN design space which have not been explored yet
  Memory optimizations
    Memory accesses are bottleneck in DNN but maybe not explored enough yet
    Apply (extended) memory access optimizations to DNN

## Slide 52: Plan
Get HLS-synthesizable C code for DNN
  At first, simple one is better to proceed
Define a target system architecture
List up and survey of most relevant DNN accel. work
  State-of-the-art system architectures, DSE
  State-of-the-art optimizations
Research
  System level Design Space Exploration of DNN C code with Aladdin-gem5
  Further effective optimization of DNN C code for HLS
    Ideas from Post-quantum cryptography (Hamid)
    Ideas from memory access optimizations for HLS
    Automate them if possible

## Slide 53: Get HLS-synthesizable C code for DNN
Possible candidates
  TensorFlow, Caffe
    Strength: Complete framework used by many organizations
    Weakness: may not be easy to rewrite the C++ into HLS-aware C
  YOLO
    Strength: Complex application (image detection) written in C
    Weakness: may not be easy to rewrite the code into HLS-aware C
  GUINESS
    Strength: Generates HLS-friendly simple C code, easy to modify
    Weakness: Simple network (good starting point), binarized only
    Provides both learning and inference
    Network with conv layer (binalized), pooling layer supported

## Slide 54: Basic Element of Neural Networks
Neuron
  Multiply and Addition
  Simple Non-linear element
f
Notes: In neurons, each input x0, x1, … are multiplied by weights w0, w1, … and are summed up. So, in neural networks, a neuron basically does multiplication and addition. The results of the summation go through non-linear unit f and becomes the output of the neuron. Several non-linear activation functions exist, but Rectified Linear Unit (ReLU) is one of the most used activation functions, and it’s very simple. In this way, a neuron accepts inputs and generates an output value.

## Slide 55: Basic (and abstract) Neural Network
Neurons are connected layer-by-layer.
Weights are computed by training with large data set.
Using neural network for classification is called inference.
Ex.
Input
image
Classification/
prediction
Results
(Cat, Dog, …)
Pixel
value
w1
w0
(More than one hidden layers)
Notes: Each neuron explained in the previous slide are connected layer-by-layer. More specifically, the output value of a neuron becomes an input value of the other neuron in the next layer

## Slide 56: Fully connected layer
Ex. Convolutional
layer
DNN usually fully connected layer at the last stages
  Weights contains many zeros, leading to sparse matrix multiply
  Fully-connected and Sparsely-connected shows different characteristics

## Slide 57: Implementation detail (Vivado HSL pragma)
Since each layer uses input buffer
func_A, B, C represents
Nested loops for CNN layers
#pragma HLS dataflow

## Slide 58: Example CNN (ResNet)
Sequences of the same or similar CONV layers are also used

## Slide 59: Experiments
VGGNet-E (VGG19)
  fuse the following layers
    first 5 conv + 2 pooling (DAC 2017, MICRO 2015)
      Conv layers include ReLU and padding
      (Probably, because of lack of resources, stop by 5 conv layers)
AlexNet
  fuse the following layers
    5 conv + 3 pooling (DAC 2017)
    2 conv + 2 pooling (MICRO 2015)
      neglecting normalization phase (incorporated in weights)

## Slide 60: Background
Utilizing Winograd algorithm
Because of lack of bandwidth
Peak performance by the available hardware
Peak performance by the off-chip bandwidth