## Slide 1: Research status on DNN accelerator
Kenshu Seto

## Slide 2: Summary of the project (As of April 10, 2018)
Problem
  Many accelerator exists, but mostly based on fixed hardware templates
  DNN models changing, so fixed hardware template may be suboptimal
  Need to provide a efficient framework which generates the best DNN accelerator for ever-changing DNN models
Solution
  Given a DNN model, generate HLS and optimizer friendly C code
    C code more flexible than RTL code
  With the code, explore design space and generate the best one
Key techniques
  gem5-Aladdin
    System level performance estimation of accelerators with caches/scratchpads
    Explore DNN design space which have not been explored yet
  Memory optimizations
    Memory accesses are bottleneck in DNN but maybe not explored enough yet
    Apply (extended) memory access optimizations to DNN

## Slide 3: Plan (As of April 10, 2018)
Get HLS-synthesizable C code for DNN
  At first, simple one is better to proceed
Define a target system architecture
List up and survey of most relevant DNN accel. work
  State-of-the-art system architectures, DSE
  State-of-the-art optimizations
Research
  System level Design Space Exploration of DNN C code with gem5-Aladdin
  Further effective optimization of DNN C code for HLS
    Ideas from Post-quantum cryptography (Hamid)
    Ideas from memory access optimizations for HLS
    Automate them if possible

## Slide 4: Outline
Brief introduction on CNN
Most relevant related work
    Optimizing FPGA-based Accelerator Design for Deep Conv. Neural Networks, C. Zhang et al., (FPGA 2015)
    Fused-Layer CNN Accelerator, M. Alwani et al., (MICRO 2015)
    Exploring Hetero. Algorithms for Accelerating Deep Conv. Neural Networks on FPGAs. Xiao et al.,(DAC 2017)
Ongoing work on DNN accelerator

## Slide 5: Brief introduction on Convolutional Neural Networks (CNNs)
Source:
Tutorial slides from “Hardware Architectures for Deep Neural Networks”, ISCA 2017
“Efficient Processing of Deep Neural Networks: A Tutorial and Survey,” V. Sze et al., Proceedings of the IEEE, 2017

## Slide 6: Convolutional Neural Networks (CNNs)
CNNs used in various image recognitions tasks.
CNNs composed of simple layers
  {Convolution, Activation, Pooling, Padding, etc. }
Convolutions accounts for more than 90% of overall computation

## Slide 13: CONV Layer C Reference implementation
Can be a starting point for a template C code for HLS
Opportunity for loop optimization
(assume N=1 in this work)

## Slide 14: Pooling (POOL) Layer
Down-sampling images

## Slide 15: POOL Layer C Reference implementation
Simple C code
R, S: pooling window size
U : stride

## Slide 16: Example CNN (VGG16, 2014)
Consists of only CONV and Pooling layers
  Fully connected (FC) layer (currently, out of scope)

## Slide 17: Optimizing FPGA-based Accelerator Design for Deep Convolutional Neural Networks C. Zhang et al., (FPGA 2015)
Notes: This MICRO paper reduces the off-chip RAM access by placing the intermediate data between CNN layers on on-chip memory.

## Slide 24
Problem: Many off-chip data-transfers
between layers

## Slide 26: Fused-Layer CNN Accelerators M. Alwani et al., (MICRO 2015)
Notes: This MICRO paper reduces the off-chip RAM access by placing the intermediate data between CNN layers on on-chip memory.

## Slide 27: Data transfers in VGG19
Lots of transfers between early layers
  Leading to high energy consumption
(note: VGG19 is a bit old. May exhibit different tendency in Recent DNN)

## Slide 28: Off-chip transfers are energy consuming
Previous work use off-chip memory to store all data
  Motivation: Store data in on-chip memory to reduce energy
Many data transfer
between early layers
Many weights transfer
In later layers

## Slide 29: Main idea: Pyramid
output pixel depends on a set of tile-shaped data from previous layers
  like a pyramid
Store all intermediate data in on-chip RAMs instead of off-chip RAMs
Reuse on-chip data to reduce data-transfer
channel
Pyramid top
Pyramid base
Notes: In order to generate an output pixel 1, tile-shape of pixels in the preceding layers over channels are used. So, the required data to compute an output pixel become a pyramid-like shape. When next output pixel 2 is computed, we don’t need to load whole data of the tile 2, since we can reuse the data in tile 1. So, only the new data for the tile 2 can be loaded from memory.

## Slide 30: Proposed code for CONV layer
Simple C code
Tile loop for
input/output
channels
loop of
tiled images
loop for kernel
input channel loop (tiled)
output channel loop (tiled)

## Slide 31: Design Space Exploration of a CONV layer
Resource and cycles estimated from C code
  Tile size Tm and Tn of output/input channels
Area constraint
Cycle counts
=
Tc
=
Tr
Assumption
Unrolled
loop body
takes 1 cycle

## Slide 32: Task level pipelining
Each layer is a pipe stage
  Layers connected by double buffers
  Pipeline initiation interval(II) equals to max stage time
Minimize II by changing Tm and Tn
  Latency-minimized solution found by exhaustive search
II
Stage time
# pyramids
(64*64
for example)
Total latency

## Slide 33: Implementation of Task-level pipelining
Put “#pragma HLS dataflow”
Iterations in output pixels
(Pyramid top points)

## Slide 34: Reuse layers
Data are minimally copied between layers
Only new
data are
computed
Only new
data are
copied

## Slide 35: FPGA Evaluation with Vivado HLS
Compare Fused-layer and Previous design for VGG19
  The same number of DSP resources between the two
Fused-layer fused first 5 CONV layers in VGG19
Previous design iteratively execute each layer
  All data stored in off-chip memory
rougly
the same
DRAM bandwidth
significantly
reduced

## Slide 36: Note on MICRO2015 paper
Pioneering work on fused CNN accelerator
Task level pipelining
  Executes a set of sequential loops in parallel
  Has similar effects as loop fusion
Large buffer size (memory overhead)
  Large pyramid base size when many layers fused
  Layers connected with double buffer

## Slide 37: Exploring Heterogeneous Algorithms for Accelerating Deep Convolutional Neural Networks on FPGAs. Xiao et al., (DAC 2017)
Notes: This is an paper that proposes the use of line buffers between fused layers.
This paper also proposes method to generate optimal fused architecture (where to fuse, including where
To use Winograd) under resource constraints in FPGAs.

## Slide 38: Winograd algorithm for CONV layer
Reduces DSP (multiplier) units by ¼
  Uses more complex algorithm
  Requires 4x higher bandwidth
Utilize Winograd algorithm in fused CNNs
“Evaluating Fast Algorithms for Convolutional Neural Networks on FPGAs,”, FCCM 2017

## Slide 39: Framework overview
Commonly observed framework...
Vivado
HLS
#Block RAMs,
#DSP units
Off-chip bandwidth,
fusion architecture
Line buffer type
Previous type
Parametrized
library
Design Space
Exploration
Design
point
DNN spec.

## Slide 40: Proposed Design Space Exploration
Objective
  Minimize latency of total execution
  Under Resource R and data-transfer T constraints
For each layer, determine
  Fusion group (layers in the same group are fused)
    reduce I/O bandwidth but increase on-chip RAM size
    Different groups execute exclusively and share resources
  CONV algorithm type: Conventional or Winograd
  Parallelism
    Loop unroll factor, or # of data-path lanes
Solved by dynamic programming and branch-and-bound

## Slide 41: C code generation for HLS with templates
After design space exploration, optimal C code for HLS is generated with appropriate parameter setting

## Slide 42: Another idea: Use line buffer in Pyramid
Use Pyramid in MICRO2015 but without buffer management
  Computation reuse between pyramid not described (causes a lot of overhead)
Within Pyramid, line buffers are used (How to do that is unclear)
(ex. conv1)
channel x
We can reduce input/output buffers with streaming!

## Slide 43: Result for VGG19 (First 7 layers)
Used Vivado HLS
Transfer constraint
  2MB
    All layers fused
  34MB
    All data can be stored in off-chip
    More chance to use Winograd
With Winograd, higher performance achieved
Previous work [1]: MICRO2015 paper

## Slide 44: Note on DAC2017 paper
Used Winograd algorithm in fused CNN
  Improved performance with area-efficient CONV
Extended MICRO2015 with line buffers in pyramids
  Detail not described
Requires large I/O buffers in each layer
We can reduce the I/O buffers with streaming interface

## Slide 45: Ongoing work on DNN accelerator

## Slide 46: Streaming-based DNN accelerator for reducing on-chip memory
CNN powerful for image recognition tasks.
Various CNN accelerators have been proposed.
Fused CNN accelerator is an effective CNN accelerator architecture to reduce off-chip RAM accesses
Although fused CNN accelerator reduces off-chip RAM accesses, large size of on-chip RAMs are required
In this work, we propose a method to reduce on-chip RAM size with compiler transformations that enable streaming interface

## Slide 47: General DNN accelerator tool
DNN
Description
HLS
RTL of
DNN
(Ideal)
DNN accelerator implementation
tool
Compiler backend
Code for
GPU,
CPU,
distributed
computing
Parametrized
code/architectural
template
Programmable
DNN accelerator
Program for
DNN accelerator
Design Space
Explorer
Target &
resource &
constraints
description
RTL,
code
Target
scope
DNN
Application
Development
Environment
(TensorFlow, Keras, …)
ASIC,
FPGA
Given DNN descriptions, quickly generate efficient DNN accelerators satisfying constraints
HLS
code

## Slide 48: Overall picture (more focused)
Action items
  Define DNN description (subset)
  Develop C templates (and optimize it)
  Develop C code generator for DNN C code
  Develop DSE
DNN
Description
Optimized
C templates
conv, pool…
C code genarator
HLS
RTL of
DNN
Design Space Exploration
(Analytical model)
FPGA
ASIC
C code used
as intermediate
language
Target &
resource &
constraints
description
Optimized
DNN
C code

## Slide 49: What have been done so far (1/2)
Made reference C programs for DNN
  Applied loop fusion and scalar replacement to two Conv layers
    Large changes in loop size prevent fusing all loops in DNN
Literature in-depth survey (applying loop fusion in mind)
  Literatures
    Efficient Processing of Deep Neural Networks: A Tutorial and Survey, V. Sze et al., Proceedings of the IEEE, 2017
      Found work on Fused CNN accelerator
    Fused-Layer CNN Accelerators, M. Alwani et al., MICRO 2015
    Exploring Heterogeneous Algorithms for Accelerating Deep Convolutional Neural Networks on FPGAs. Xiao et al., DAC 2017
  Found
    Task-level pipelining useful for parallel execution of layers
    Room for improvement in memory size reduction

## Slide 50: Speedup by Task-level pipelining
Execute next layers as soon as input data are produced
func_A, B, C represents
Nested loops for CNN layers
#pragma HLS dataflow

## Slide 51: What have been done so far (2/2)
Take a brief look at DNN designs from Xilinx
  Uses stream interface
  Unfortunately, only for binary NN and Quantized NN with1 bit weights, 2 bit activations
    https://github.com/Xilinx/BNN-PYNQ
    https://github.com/Xilinx/QNN-MO-PYNQ
Investigate Vivado HLS with a simple example
  Usage, restriction on HLS DATAFLOW, hls::stream interface, ARRAY_PARTITION
  Find tricky things (handling of weights)
Optimized reference DNN programs to use stream interface for parallelization
  Successful for first two layers (will be successful for other layers, too)

## Slide 52: For efficient stream execution
Input
Feature
map
①
②
③
④
⑤
⑥
⑦
⑧
Output
Feature
map
①
②
③
④
⑤
⑥
⑦
⑧
Input/output of DNN layers: 3D images
Want to arrange loops of all layers so that
  Outputs are generated in the same order of inputs
Reduce “wait” and buffer size
A loop nest of DNN
Layer

## Slide 53: Optimized C template
Applied loop interchange , unrolling, fusion, etc.
void Conv2D_1(int I[8][16][16], int W[8][8][3][3], int B[8], DATA_T O[8][16][16] {
int m, x, y, i, j, k;
int ifm, ofm;
for (m=0; m<8; m++) {
for (x=0; x<16; x++) {
for (y=0; y<16; y++) {
ofm = B[m];
for (k=0; k<8; k++) {
for (i=0; i<3; i++) {
for (j=0; j<3; j++) {
if (x+i < 16 && y+j < 16) {
ifm = I[k][x+i][y+j];
} else {
ifm = 0; // zero padding
}
ofm = ofm + ifm * W[m][k][i][j];
}
}
}
if (ofm < 0) { // relu activation
ofm = 0;
}
O[m][x][y] = ofm; } } } }
void Conv2D_1(int I[3][16][16], DATA_T W[8][3][3][3], int B[8], hls::stream<int> &O_strm) {
int m, x, y, i, j, k;
int ifm, ofm;
int I_0, I_1, I_2, I_3, I_4, I_5, I_6, I_7, I_8;
for (x=0; x<16; x++) {
for (y=0; y<16; y++) {
for (k=0; k<3; k++) {
I_0 = I[k][x+0][y+0];
I_1 = I[k][x+0][y+1];
...
I_8 = I[k][x+2][y+2];
for (m=0; m<8; m++) {
if (k==0) ofm = B[m];
else ofm = O_buf[m];
if (x < 16 && y < 16) ifm = I_0;
else ifm = 0; // zero padding
ofm = ofm + ifm * W[m][k][0][0];
if (x < 16 && y+1 < 16) ifm = I_1;
else ifm = 0; // zero padding
ofm = ofm + ifm * W[m][k][0][1];
...
if (k<2) O_buf[m] = ofm;
else if (k==2) O_strm.write(ofm);
} } } } }

## Slide 54: Simulation of Optimized C template
By optimization, two layers are executed in parallel
Before optimization
After streaming optimization

## Slide 55: C code generator and format for DNN description
Layer # | Layer Type | Name | M | C | H | W | R | S | E | F | U | Padding | Activation | bias | M | F | E | R | S | U | Padding | Pooling Type
1 | Conv2D | block1_conv1 | 64 | 3 | 224 | 224 | 3 | 3 | 224 | 224 | 1 | same | relu | Yes |  |  |  |  |  |  |  | 
2 | Conv2D | block1_conv2 | 64 | 3 | 224 | 224 | 3 | 3 | 224 | 224 | 1 | same | relu | Yes |  |  |  |  |  |  |  | 
3 | MaxPooling2D | block1_pool |  |  |  |  |  |  |  |  |  |  |  |  | 64 | 112 | 112 | 2 | 2 | 2 | No | Max
4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Excel file describing, ex, VGG19
Or, Text file (Json file, xml file, anything) for VGG19
LayerNo=1, LayerName=block1_conv1, LayerType=Conv2D, M=64, C=3, H=224, …,
LayerNo=2, In1=1, LayerName=block1_conv2, LayerType=Conv2D, M=64, C=3, H=224, …,
LayerNo=3, In1=2, LayerName=block1_pool, LayerType=MaxPooling2D, M=…
C program for
VGG19
accelerator
C program for
VGG19
Test bench
C code
generator
Can be used for many research on DNN accelerators

## Slide 56: Example Keras description (VGG19)
Extract DNN description for C code generation from Keras

## Slide 57: Other DNNs in Keras
To handle them, following layers must be supported for code generator
Shortcut, branch not supported by Vivado HLS DATAFLOW
Network | Layers, constructs to be supported
ResNet50 | add layer, shortcut construct
densenet | concatenate layer
Mobilenet | DepthwiseConv2D layer
Inception v3 | concatenate layer, branch construct
Xception | SeparableConv2D layer

## Slide 58: ResNet50 (popular DNN with 50 layers)
Workaround necessary to handle “Shortcut”
Shortcut

## Slide 59: Action items (1/2)
C code generation (Jiyoung, Sujin)
  Keras (Python) to DNN description (text format or Excel file)
    VGG19, ResNet50, (Inception v3, densenet, …)
  DNN C code generation from DNN description
Verification of DNN C code (Hamid)
  It is necessary to verify the equivalence between Keras and C
    Need to incorporate batch normalization layers into Conv layers
    Need to output weights and intermediate images
Optimized C template (Kenshu)
  Pooling, activation with streaming
Define DNN description format for more complex DNN
  That can handle merge and branch in ResNet, Inception

## Slide 60: Action items (2/2)
Implementation of previous work for comparison
  MICRO 2015 or DAC2017 (detail unclear)
Experimental Evaluation with Vivado HLS
  BRAMs, Logic element, execution cycles
  Issue: In ASICs, minimizing on-chip RAM usage is very useful, but for FPGA, it is O.K if constraints on BRAM is satisfied
  Comparison against MICRO 2015 or DAC 2017
  FPGA board necessary for C-RTL co-simulation
    Software RTL simulation extremely slow
    FPGA board should be large enough to execute whole DNNs
Design Space Explorations (Tile size, unroll factor)
  Analytical model?
  Unfortunately, we cannot use gem5-Aladdin for task-level pipelined C code …
More survey on related works to put in the publication

## Slide 61: Supplementary slides

## Slide 62: Research project at DRG: Design space exploration and memory access optimization for Deep Neural Network (DNN)

## Slide 63: Research plan
Develop template C code
  Easier for loop optimization (fusion) and memory optimization
  Conv (different strides with Activation), Pooling
Develop a generator tool
  that generate C code from DNN descriptions
  Keras can be used as DNN descriptions
Optimize the generated C code manually or semi-automatically
  Loop fusion, interchange, tiling, …
  Buffer optimization
Run gem5-Aladdin for estimation
  only for single thread code
Synthesize with Vivado-HLS
  Use #pragma HLS DATAFLOW to do task level pipelining
  Implement the previous work (DAC2017, MICRO 2015) and compare the results (resource, #cycles, etc)

## Slide 64: Summary of the project
Problem
  Many accelerator exists, but mostly based on fixed hardware templates
  DNN models changing, so fixed hardware template may be suboptimal
  Need to provide a efficient framework which generates the best DNN accelerator for ever-changing DNN models
Solution
  Given a DNN model, generate HLS and optimizer friendly C code
  With the code, explore design space and generate the best one
Key techniques
  gem5-Aladdin
    System level performance estimation of accelerators with caches/scratchpads
    Explore DNN design space which have not been explored yet
  Memory optimizations
    Memory accesses are bottleneck in DNN but maybe not explored enough yet
    Apply (extended) memory access optimizations to DNN

## Slide 65: Plan (As of April 10, 2018)
Get HLS-synthesizable C code for DNN
  At first, simple one is better to proceed
Define a target system architecture
List up and survey of most relevant DNN accel. work
  State-of-the-art system architectures, DSE
  State-of-the-art optimizations
Research
  System level Design Space Exploration of DNN C code with gem5-Aladdin
  Further effective optimization of DNN C code for HLS
    Ideas from Post-quantum cryptography (Hamid)
    Ideas from memory access optimizations for HLS
    Automate them if possible

## Slide 66: Get HLS-synthesizable C code for DNN
Possible candidates
  TensorFlow, Caffe
    Strength: Complete framework used by many organizations
    Weakness: may not be easy to rewrite the C++ into HLS-aware C
  YOLO
    Strength: Complex application (image detection) written in C
    Weakness: may not be easy to rewrite the code into HLS-aware C
  GUINESS
    Strength: Generates HLS-friendly simple C code, easy to modify
    Weakness: Simple network (good starting point), binarized only
    Provides both learning and inference
    Network with conv layer (binalized), pooling layer supported

## Slide 67: Basic Element of Neural Networks
Neuron
  Multiply and Addition
  Simple Non-linear element
f
Notes: In neurons, each input x0, x1, … are multiplied by weights w0, w1, … and are summed up. So, in neural networks, a neuron basically does multiplication and addition. The results of the summation go through non-linear unit f and becomes the output of the neuron. Several non-linear activation functions exist, but Rectified Linear Unit (ReLU) is one of the most used activation functions, and it’s very simple. In this way, a neuron accepts inputs and generates an output value.

## Slide 68: Basic (and abstract) Neural Network
Neurons are connected layer-by-layer.
Weights are computed by training with large data set.
Using neural network for classification is called inference.
Ex.
Input
image
Classification/
prediction
Results
(Cat, Dog, …)
Pixel
value
w1
w0
(More than one hidden layers)
Notes: Each neuron explained in the previous slide are connected layer-by-layer. More specifically, the output value of a neuron becomes an input value of the other neuron in the next layer

## Slide 69: Fully connected layer
Ex. Convolutional
layer
DNN usually fully connected layer at the last stages
  Weights contains many zeros, leading to sparse matrix multiply
  Fully-connected and Sparsely-connected shows different characteristics

## Slide 70: Experiments
VGGNet-E (VGG19)
  fuse the following layers
    first 5 conv + 2 pooling (DAC 2017, MICRO 2015)
      Conv layers include ReLU and padding
      (Probably, because of lack of resources, stop by 5 conv layers)
AlexNet
  fuse the following layers
    5 conv + 3 pooling (DAC 2017)
    2 conv + 2 pooling (MICRO 2015)
      neglecting normalization phase (incorporated in weights)

## Slide 71: Background
Utilizing Winograd algorithm
Because of lack of bandwidth
Peak performance by the available hardware
Peak performance by the off-chip bandwidth

## Slide 74
Weights in DNN are usually pruned
  60-70% reduction in Conv layers, 90% reduction in FC layers
  Sparse weights corresponds to sparse matrix multiplication
  Weights are not always sparse, and sparse

## Slide 75: Tensor Comprehension

## Slide 76: Related work

## Slide 77: Recent research on CNN accelerators

## Slide 78: Summary

## Slide 80: Convolution (CONVL) Layer computation (1 layer)
For each output pixel, do the following computation

## Slide 82: Symbols used in the implementation code
Elaborately developed to maximize reuse
row, col:
Coordinate of
Pyramid top
Sx, Sy:
stride of the adjacent
pyramid base

## Slide 83: Result for AlexNet (5 CONV + 3 Pool)
    All layers fused
    Compared to MICRO2015, 1.24X speedup
      DSPs saved by Winograd algorithm are utilized by conventional CONV layers to enhance performance