## Slide 1: Source-level optimizations for high-level synthesis (HLS)
Kenshu Seto

## Slide 2: Source-level code tuning for HLS
Usually required to maximize performance in HLS
  Time consuming
  Users of HLS are not expert in complex code tuning
Automatic source code optimization is important for wider acceptance of HLS
  Shorten time-to-market further
Such code tunings include
  Loop / memory / interface optimizations
I’ve been working on automating them
for ( …)
for ( … )
S1;
for( … )
for( … )
S2;
HLS
Logic
Syn.
input …
output…
always @
begin
…
end
Source-level
compiler optimizations
H/W
block
H/W
block
Mem
Mem
High-performance H/W
for ( …)
for ( … )
S1;
S2;

## Slide 3: Various loop optimizations
Some loop optimizations are depicted below
Want to apply the best combination for optimal HLS results
for (i=1; i<=N; i++)
Y[i] = Z[i];
for (j=1; j<=N; j++)
X[j] = Y[j];
for (i=1; i<=N; i++) {
Y[i] = Z[i];
X[j] = Y[j];
}
loop fusion
for (i=1; i<=N; i++) {
Y[i] = Z[i];
X[j] = Y[j];
}
for (i=1; i<=N; i++)
Y[i] = Z[i];
for (j=1; j<=N; j++)
X[j] = Y[j];
loop distribution
for (i=1; i>=N; i++)
Y[N-i] = Z[i];
for (j=0; j<=N; j++)
X[j] = Y[j];
for (i=N-1; i<=0; i--)
Y[i] = Z[N-i];
for (j=0; j<=N; j++)
X[j] = Y[j];
loop reversal
for (i=1; i<=8; i++)
for (j=1; j<=8; j++)
x = x + Y[i]*Z[i];
for (t=1; t<=64; t++) {
i = …; j = …;
x = x + Y[i]*Z[i];
}
loop flattening
for (i=1; i<=N; i++)
for (j=0; j<=M; j++)
Z[i][j] = Z[i-1][j];
for (j=0; j<=M; j++)
for (i=1; i<=N; i++)
Z[i][j] = Z[i-1][j];
loop interchange
for (i=1; i<=N; i++) {
Y[i] = Z[i];
}
for (i=0; i<=N-1; i++) {
Y[i+1] = Z[i+1];
}
loop shifting

## Slide 4: Combination of loop optimizations
Loop fusion is effective for a sequence of loops
  Such as image processing / matrix computation programs
Challenge: What and which order should we apply loop opts.? ⇒Polyhedral approach is one of the most advanced ways
Loop shifting
Extend loop bounds
Loop fusion
Memory access optimization
Loop pipelining

## Slide 5: Concept of polyhedral-based optimizations
Extract polyhedral model from input C program
  C programs are limited to a subset (static control parts)
  Extract data-dependency between statements
Perform loop optimizations on the polyhedral model
  Multiple loop optimizations such as loop shift, interchange, fusion are applied at the same time in the model
  Powerful to obtain the optimal loop structure
for ( i=0; i<4; i++)
for ( j=0; j<4; j++)
S1: A[ i ][ j ] = A[ i ][ j ]+１;
for ( i=0; i<4; i++)
for ( j=0; j<4; j++)
S2: x[ i ] = x[ i ]+A[ j ];
Input C code
j
i
S1
j’
i’
S2
Polyhedral model
t2
t1
S1
Loop
Optimizations
Pluto
S2
Optimal
Combination of
Loop opts.
Polyhedral
model
Extraction
Clan
Polly
PPCG
for (t1=0; t1<4; t1++)
for (t2=0; t2<5; t2++) {
if (t2 < 4)
A[t2,t1] = A[t2,t1]+1;
if (t2 > 0)
x[t1] = x[t1]+A[t2-1];
}
Code
Gen.
CLooG
ISL
Optimized loop
Polyhedral optimizations proposed for
SIMD, GPU, …

## Slide 6: Static Control Parts (SCoP): Target of polyhedral optimization
Following items represented by the linear expression of loop indices
  Loop bounds
    for (j=0; j<i+1; j++)
  if conditionals
    if (i >= 2*j+k+1)
  Array subscripts
    B[i][j+2]
Extensions of SCoP were proposed
for(i=0; i<8; i++)
for(j=0; j<8; j++){
for(k=0; k<8; ++k)
if (k==0) B[i][j]=0;
for(k=0; k<8; ++k)
B[i][j] = B[i][j] + A[i][k];
}
for(i=0; i<8; i++)
for(j=0; j<8; j++){
for (k=0; k<8; ++k)
if (k==0) D[i][j] = D[i][j];
for(k=0; k<8; ++k)
D[i][j] = D[i][j] + B[i][k];
}

## Slide 7: Polyhedral-based Loop Fusion with Outer Loop Shifting for High-level Synthesis
[3] Y. Kato and K. Seto, “Loop fusion with outer loop shifting for high-level synthesis,” IPSJ Trans. on SLDM, 2013

## Slide 8: Advantage of loop fusion for accelerator synthesis
・ merges a sequence of loops into a single fully nested loops.
・ usually involves other loop transformations such as loop interchange, etc.
・ boosts performance by increasing parallelism before high-level synthesis .

## Slide 9: Previous polyhedral-based loop fusion : Pluto [1]
・ uses polyhedral model to represent loops and loop transformations.
・ reorders stmt. instances to enhance both outer parallelism and data locality.
・ emphasize on outer parallelism which causes negative impact on HLS.
[1] Bondhugula, et al. “"A Practical and Automatic Polyhedral Program Optimization System,” PLDI 2008

## Slide 10: Loop fusion with Outer Loop Shifting (OLS) [2]
[3] Y. Kato and K. Seto, “Loop fusion with outer loop shifting for high-level synthesis,” IPSJ Trans. on SLDM, 2013
・ Outer Loop Shifting (OLS) modifies schedule produced by Pluto to facilitate loop fusion.
・ Constants in “scalar dimensions” are added to outer “loop dimension” when legal.

## Slide 11: Experimental results

## Slide 12: Scalar Replacement with polyhedral model for Hardware Synthesis
[3] K. Seto, “Scalar Replacement with polyhedral model for Hardware Synthesis,”
Submitted to IPSJ Trans. on SLDM

## Slide 13: High-level synthesis and necessity of code tuning
High-level synthesis (HLS)
  Vivado HLS(Xilinx), HLS compiler (Intel), Stratus (Cadence), CyberWorkBench (NEC)
  Significantly reduces hardware design time
  Time-consuming tuning is necessary for optimized RTL
Optimized
C/C++
for HLS
Algorithm
C/C++
Manual code tuning
High-level synthesis
Optimized RTL
Automatic code tuning is a
key to further enhancing HLS
Effective memory access optimizations
  Memory partitioning
    Partitions local memory to increase memory ports and bandwidth
  Scalar replacement (window buffering)
    Replaces repeated memory accesses into (shift) register accesses
Notes: There are quite a few high-level synthesis tools out there.
They significantly reduce RTL coding time.
Unfortunately, time-consuming manual tuning is often necessary to obtain optimized RTL with HLS tools
and such tuning lowers the advantages of HLS tools.
Automating code tuning is a key to further enhancing the advantage of HLS tools
Memory access optimizations are one kind of such code tuning in HLS.
#Memory access optimizations includes memory partitioning and scalar replacement.
#Memory partitioning partitions a local memory into multiple banks in order to increase memory ports and hence memory bandwidth.
Scalar replacement, also called window buffering, replaces repeated memory accesses into register accesses.

## Slide 14: Scalar replacement (SR)
In HLS, large arrays are mapped to local memories
  int A[64][64];
SR replaces array accesses with scalar variable accesses
  Completely eliminates local memories and memory access conflicts
    Chip area reduction and latency reduction
Byoungro So et al., “Increasing the applicability of Scalar replacement”, Compiler Construction, 2004
for (i=0; i<n; i++) {
A[i+2] = in[i];
out[i] = A[i+2]+A[i+1]+A[i];
}
for (i=0; i<n; i++) {
a0 = in[i];
out[i] = a0+a1+a2;
a2 = a1;
a1 = a0;
}
Scalar
Replacement
(SR)
Previous SR methods cannot handle real-life code including accesses with constant subscripts (ex. A[0], B[i][64]).
Shift
registers
Notes: Please note that in HLS, large arrays are mapped to local memories which have limited I/O ports, typically, at most two.
#Scalar replacement replaces array accesses with scalar variables, so that local memories and #memory access conflicts are completely eliminated. So, scalar replacement reduces both chip #area and latency.
I will explain scalar replacement with an example.
In the example on the left, the code has four array accesses to array A.
By applying scalar replacement to the code, all the array accesses are replaced with scalar variables, a0, a1, a2.
Scalar variables a0, a1, a2 are shifted in each iteration of the loop.
After scalar replacement, array A is completely removed.
Differently from local memories with limited number of I/O ports, scalar variables provides unlimited number of parallel accesses.
So, scalar replacement reduces both chip area and latency.
Unfortunately, previous scalar replacement methods cannot handle real-life code including accesses with constant subscripts.

## Slide 15: Scalar replacement with polyhedral model
For subsets of C code, we completely analyze reuses between array accesses including constant subscripts.
  We take conditions in If-statements into consideration in the analysis.
  The analysis is based on polyhedral model.
We utilize the reuse information table in code generation.
1 for(y=0; y<=9; y++){
2 for(x=0; x<=9; x++){
3 A[y][x] =……;
4 …
5 if (y>=1) {
6 if (y<=2) t+= A[0][x];
7 …
8 } } }
 | Access type | Array access | Reuse distance | Scalar variable | Reuse condition
1 | Generator | A[y][x] | d1=0 | S0 | always
2 | … | … | … | … | …
3 | Reuse | A[0][x] | d3=10 | s10 | y==1
4 | Reuse | A[0][x] | d4=20 | s20 | y==2
5 | … | … | . | … | …
1 for(y=0; y<=9; y++){
2 for(x=0; x<=9; x++){
3 s0=……;
4 …
5 if (y>=1) {
6 if (y<=2) {
7 if (y==1) s10_s20=s10;
8 else if (y==2) s10_s20=s20;
9 t += s10_s20;
10 }
11 …
12 }
13 s30=s29;
…..
42 s1 = s0; } }
Proposed
scalar
replacement
Notes: This is an example code including an array access with a constant subscript.
Previous scalar replacement method imposes a constraint on array accesses
That these accesses should re replaced with a single scalar variable.
Since array accesses with constant subscripts does not satisfy the constraint,
the previous scalar replacement method cannot handle array accesses with
constant subscripts.
The proposed method does not impose such constraint on array accesses,
so the array accesses with constant subscripts can be handled.
In addition, we analyze the conditions in if-statements for a subset of C code,
So that the number of multiplexers is minimized.

## Slide 16: Preliminary experimental result
Applied the proposed method to a benchmark C code
  4 image processing loop kernels were fused into a single loop.
diff
vfilter
hfilter
blend
src0
src1
tmp0
tmp1
tmp2
out
 | Execution cycles [cycles] | #gates [gates] | Memory size [bit] | Shift register size [bit]
Previous | 5.4M | 15k | 192M | 0
Propoed | 1.9M | 59k | 0 | 308K
Synthesized optimized C code into gates with HLS
  Local memories (tmp0, 1, 2) were completely eliminated.
  Execution cycles and memory size were significantly reduced.
Notes: We applied the proposed scalar replacement method to a benchmark C code including constant array subscripts.
The code is a single doubly-nested loop which was made by fusing 4 image processing loop kernels.
The optimized code obtained by applying the proposed scalar replacement was synthesized with a commercial
high-level synthesis tool. After the optimization, large local memories corresponding to the local temporal arrays
tmp0, tmp1, and tmp2 were removed and smaller shift register were introduced instead.
Execution cycles were significantly reduced because memory access bottlenecks to the local memories
were eliminated. # of gates increased because of the enabled parallel execution.
Thank you for your attention.

## Slide 17: Research project at DRG: Design space exploration and memory access optimization for Deep Neural Network (DNN)

## Slide 18: Summary of the project
Problem
  Many accelerator exists, but mostly based on fixed templates
  DNN models are changing, so fixed template may be suboptimal
  Need to provide a efficient framework which generates the best DNN accelerator for ever-changing DNN models
Solution
  Given a DNN model, generate HLS and optimizer friendly C code
  With the code, explore design space and generate the best one
Key techniques
  Alladin-gem5
    System level performance estimation of accelerators with caches/scratchpads
    Explore DNN design space which have not been explored yet
  Memory optimizations
    Memory accesses are bottleneck in DNN but maybe not explored enough yet
    Apply (extended) memory access optimizations to DNN

## Slide 19: Plan
Get HLS-synthesizable C code for DNN
  At first, simple one is better to proceed
Define a target system architecture
List up and survey of most relevant DNN accel. work
  State-of-the-art system architectures, DSE
  State-of-the-art optimizations
Research
  System level Design Space Exploration of DNN C code with Aladdin-gem5
  Further effective optimization of DNN C code for HLS
    Ideas from Post-quantum cryptography (Hamid)
    Ideas from memory access optimizations for HLS
    Automate them if possible

## Slide 20: Get HLS-synthesizable C code for DNN
Possible candidates
  TensorFlow, Caffe
    Strength: Complete framework used by many organizations
    Weakness: may not be easy to rewrite the C++ into HLS-aware C
  YOLO
    Strength: Complex application (image detection) written in C
    Weakness: may not be easy to rewrite the code into HLS-aware C
  GUINESS
    Strength: Generates HLS-friendly simple C code, easy to modify
    Weakness: Simple network (good starting point), binarized only
    Provides both learning and inference
    Network with conv layer (binalized), pooling layer supported